## Slide 1
Orbital Maneuvering - Pointing Modes
NMSU
07/16/2021
1

## Slide 2: ADCS Modes
Detumble
Sun point (Standby)
Ground station point (Communication)
GNSS receiver point (Maneuver)
Observation
**Momentum unloading by torque rods is default
**Sun pointing is the secondary requirement in the Ground station point and GNSS receiver point modes

## Slide 3: ADCS State Diagram
Based on BCT Bus Modes and Transitions
Key
Command
Autonomous
Error/Fault
Primary/Secondary pointing requirements
Standby
  Primary pointing: Solar panel to Sun
  Secondary pointing: GNSS receiver to zenith
UHF Downlink
  Primary pointing: UHF antenna to nadir
  Secondary pointing: Solar panel to Sun
Maneuver
  Primary pointing: GNSS receiver to zenith
  Secondary pointing: Solar panel to Sun
Observation
  Primary pointing: Boresight to Sun
  Inertial hold
UHF Downlink
Observation
Standby
Spacecraft Separation
Maneuver
(Transfer/
Escape/
Science)
Sun Safe
Survival

## Slide 4: GNC ConOps
Manual modes
  Startup/Recovery/Decommissioning
Standby mode
  Data downlink
Transfer mode
  Orbit reconfiguration
Science/Observation mode
  Collect science data
Escape mode
  Collision avoidance
Safe
Science
Completion
of science campaign or contingency
Formation safety compromised, error, or low power
Transfer
Science Formation established
Escape
Observation
Performing or completing science observation
Preliminary Operations
Reacquisition
Standby
Standby formation acquired
Autonomous
Modes
Manual
Modes
Key
Command
Autonomous
Error/Fault
Active Collision Maneuver
Passive Relative Orbit Geometry (200 m)
Science Relative Orbit Geometry (40 m)
No Relative Orbit Geometry
1
2
3
1
1
3
3
3
3
2
2

## Slide 5: BCT Bus Modes and Transitions (PDR)

## Slide 7: Backup Slides
7

## Slide 8
Important Pointing Vectors
8
X
Y
Z
+Y
-X
-Z
DSC Body Frame
Detector Boresight Vector = [-1, 0, 0]B
Solar Panel Normal Vector = [-sqrt(2)/2, sqrt(2)/2, 0]B
GNSS Receiver Vector = [0, 0, -1]B
(out of page vector)
Notes: 8

## Slide 9: Previous Mission Example: LightSail 2

## Slide 10: Pointing Requirements of DSC
Standby mode (data downlink)
  Primary vector: UHF antenna to nadir
  Secondary vector: Solar panel to Sun
Transfer mode (orbit reconfiguration)
  Primary vector: GNSS receiver to zenith
  Secondary vector: Solar panel to Sun
Science (collect science data)
  Primary vector: GNSS receiver to zenith
  Secondary vector: Solar panel to Sun
Observation mode (collect science data)
  Primary vector: Boresight to Sun
  Inertial hold
Escape mode (collision avoidance)
  Primary vector: GNSS receiver to zenith
  Secondary vector: Solar panel to Sun
Safe
Science
Completion
of science campaign or contingency
Formation safety compromised, error, or low power
Transfer
Science Formation established
Escape
Observation
Performing or completing science observation
Preliminary Operations
Reacquisition
Standby
Standby formation acquired
Autonomous
Modes
Manual
Modes
Key
Command
Autonomous
Error/Fault
Active Collision Maneuver
Passive Relative Orbit Geometry (200 m)
Science Relative Orbit Geometry (40 m)
No Relative Orbit Geometry
1
2
3

## Slide 11: ADCS State Diagram (Previous Idea 1)
Secondary pointing requirements
  Ground station point: Solar panel to Sun
  GNSS receiver point: Solar panel to Sun
  Sun point: GNSS receiver to zenith
  Detumble & Observation: N/A
Key
Command
Autonomous
Error/Fault
Active Collision Maneuver
Possible topics to discuss
  Combine Detumble and Sun point modes?
  Simplify transition between Ground station point & GNSS receiver point modes?
  Trigger conditions?
  Any other things…
GNSS Receiver Point
Observation
Sun Point
Ground Station Point
Detumble
Spacecraft Separation
Standby
Transfer/ Science/ Escape
Charge
Safe
Science

## Slide 12: ADCS State Diagram (Previous Idea 2)
Based on BCT Bus Modes and Transitions
Key
Command
Autonomous
Error/Fault
UHF Downlink
Observation
Sun Safe
Standby& Charge
Survival
Spacecraft Separation
Maneuver
(Transfer/
Escape/
Science)
Primary/Secondary pointing requirements

## Slide 13: Example: GNSS Receiver Point Constraints
GNSS Receiver must be ±15o of the zenith direction
Use secondary pointing requirement to maximize power generation

## Slide 14: ADCS Modes – Observation Mode
Reference frames
  Earth Sun frame (ESF)
  Radial Tangential Normal (RTN) frame
  Detector S/C (DSC) frame
  Optics S/C (OSC) frame
40 m

## Slide 16: Example of Maneuver Command
Example maneuver table
  LVLH frame
Axis definitions
R – Aligned with position vector from earth’s center
N – Aligned with orbit angular momentum vector
T – Completes right-handed triad (nominally near velocity direction)
R
N
T
Time (s) | 100 | 500 | 760.2 | 1000
R (m/s) | 0.1 | -0.2 | 0.15 | 0.4
T (m/s) | 0.4 | 0.1 | -0.2 | 0.15
N (m/s) | 0.15 | 0.4 | 0.1 | -0.2

## Slide 17
Orbit Parameters
Altitude: 550km
Sun-synchronous inclination: 97.4o
Nominal Epoch: 3/21/2024
LTAN: 9AM
  Input parameter: RAAN 315o
17
Notes: 17